## Slide 1: Navigation
References: FTGU Pages 175 - 255
CI Valentine
PO 403

## Slide 2: Review
How often are GFA’s published?
Decode this TAF
TAF CYKZ 071742Z 0718/0806 15007KT P6SM FEW020 SCT060 OVC130 PROB40 0719/0724 VRB15G25KT 2SM +TSRA BR BKN020 OVC050CB FM080000 05003KT P6SM BKN110 TEMPO 0800/0803 P6SM -SHRA BKN015 FM080300 02005KT 3SM SHRA BR OVC008 PROB30 0803/0806 VRB20G35KT 11/2SM +TSRA BR OVC006CB RMK NXT FCST BY 080000Z=
Notes: Issued 4 times a day
Terminal Area Forecast for Buttonville Airport Issued on the 7th at 1742 Zulu For use on the 7th at 1800Zulu to the 8th at 0600Zulu Winds forecast to be 150 degrees True at 7 knots Visibility forecast greater than 6 statute miles Few clouds forecast at 2000 feet above ground level Scattered clouds forecast at 6000 feet above ground Overcast clouds forecast at 13000 feet above ground 40% probability between 7th from 1900-2400 Zulu that: Winds will be variable direction at 15 knots gusting to 25 knots Visibility will be 2 statute miles There will be thunderstorms and heavy rain and mist Ceiling will be broken at 2000 feet above ground and Clouds will be overcast at 5000 feet above ground due to cumulonimbus From the 8th at 0000 Zulu Winds are forecast 050 degrees true at 3 knots Greater than 6 statute mile visibility is forecast Clouds forecast broken at 11000 feet above ground 50% chance during 8th between 0000-0300 Zulu that Greater than 6 statute miles visibility Light rain showers Broken ceiling at 1500 feet above ground From the 8th at 0300 Zulu Winds forecast 020 degrees true at 5 knots Visibility forecast 3 statute miles Forecast rain showers and mist Clouds forecast overcast at 800 feet above ground 30% chance during 8th from 0300-0600Zulu Winds variable direction at 20knots gusting to 35 knots Visibility 1 and ½ statute miles Thunderstorms and heavy rain and mist Ceiling overcast at 600 feet above ground due to cumulonimbus Next forecast by the 8th at 0000Zulu

## Slide 3: Topics to be covered today
Definitions
Latitude and Longitude
Earth’s Magnetism
Compass Errors
Projections

## Slide 4: Headings
Heading
  The direction in which the aircraft’s longitudinal axis is pointing, measured clockwise from north
True Heading
  The direction in which the aircraft nose is pointed, measured clockwise from true north
Magnetic Heading
  The direction in which the aircraft nose is pointed, measured clockwise from magnetic north
Notes: Variation is used to convert heading or bearing from true to magnetic or vice versa

## Slide 5
Compass Heading
  The direction that the needle of the compass is pointing
Variation
  The angle between a true meridian and a magnetic meridian at any point
Deviation
  The angle between magnetic heading and compass heading
  Caused by magnetic fields generated by the airframe, engine, and avionics

## Slide 6: Definitions
Direction
  Measured in degrees, numbers clockwise from North. North = 0° or 360°, East = 90°, South = 180°, West = 270°
True and Magnetic Direction
  Direction measured in degrees true when read directly from a map or in magnetic degrees when variation is considered
Magnetic Dip
  Angle between the horizontal plane and the plane of the magnet/compass under the influence of a non-horizontal magnetic line of force
Notes: Compass heading: magnetic heading corrected for deviation errors of the compass

## Slide 7: Definitions
Great Circle
  A circle on the surface of the earth whose plane passes through the centre of the earth
  It is the shortest distance between any two points on the earth
Rhumb Line
  A curved line on the surface of the earth that cuts all of the meridians at the same angle
Notes: Equator is the only line on the surface of the Earth that is both a rhumb line and a great circle at the same time!

## Slide 9: Definitions
Isogonals
  Lines on a map connecting places of equal variation
  Labeled East or West according to position relative to True North
Agonic Line
  A line connecting places of zero variation
  Two agonic lines; one in North America and one on the opposite side of the Earth
Notes: Isogonic and Agonic lines are not straight lines
They bend and twist due to the influence of local perturbations in the local magnetic field due to magnetic bodies below the Earth’s surface

## Slide 10: More Definitions

## Slide 11: More Definitions
Bearing
  The position of an object relative to the longitudinal axis of the aircraft
Nautical Mile: 6080 feet
  The average length of one minute of latitude
Statute Mile: 5280 feet
Kilometre: 3280 feet
Notes: 1 NM = 1.85 KM
1 NM = 1.15 SM
66NM = 76 SM = 122KM

## Slide 12: Speed
Knots (kts)
  Speed in nautical miles per hour
Miles per Hour (mph)
  Speed in statute miles per hour
Kilometres per Hour (km/h)
  Speed in kilometres per hour
Notes: Speed: the rate of change of position over time compared to an object at rest

## Slide 13: Speeds
Indicated Airspeed (IAS)
  The airspeed shown on the Airspeed Indicator
True Airspeed (TAS)
  Speed of the aircraft relative to the air
  Calibrated airspeed corrected for compressibility and density
Groundspeed
  Speed of the aircraft relative to the ground
Notes: Speed = Distance/Time

## Slide 14: Tracks
Track
  The intended path of the aircraft over the ground
Track Made Good
  The actual path of the aircraft over the ground
Drift
  The angle between the heading of the aircraft and the track made good

## Slide 15
Drift

## Slide 16: Cardinal Point of the Compass Rose

## Slide 17: Heading vs. Bearing


A
B
The bearing to aircraft B is 090°
Aircraft A is on a heading of 000°
000°
090°

## Slide 18: Heading vs. Bearing


A
B
The bearing to aircraft A is 180°
Aircraft B is on a heading of 090°
090°
180°

## Slide 19: Review
What is the difference between magnetic and compass heading?
What is a rhumb line?
What is the length of a nautical mile?
Notes: Compass heading is magnetic heading corrected for deviation
Curved line on the Earth’s surface which intercepts all meridians at the same angle. A straight line drawn on a Mercator projection. All parallels of latitude are Rhumb lines
1 NM = 6080 feet 1 NM = 1.85 km 1 NM = 1.15 SM 1 NM is the average length of a minute of latitude

## Slide 20: Latitude, Longitude and the Earth’s Magnetism

## Slide 21: The Earth
Earth is an oblate spheroid; a sphere flattened at the top and bottom
Surface of the globe is divide into geometrical pattern of intersecting circles called graticule

## Slide 22: Earth’s Magnetism
Earth is a giant magnet
Invisible lines of force link the two poles, creating a magnetic field which encircles the planet
Form magnetic meridians
Lines of force are horizontal, parallel with the Earth’s surface at the equator and more vertical near the poles
Notes: Magnetic North and South poles are not located at the same position as the true North and South poles
Position of the magnetic pole changes very slightly from year to year

## Slide 23: Meridians of Longitude
Semi-great circles that join the geographic poles of the earth
They are measured from 0 to 180 degrees East and West of the Prime Meridian, which runs through Greenwich, England
The meridian opposite the Prime Meridian is called the International Date Line; time changes by a day (180°)

## Slide 24: Meridians of Longitude
Longitude is measured in degrees, minutes and seconds
There are 60 minutes in a degree and 60 seconds in a minute

## Slide 26: Parallels of Latitude
Circles on the earth’s surface which lie parallel to the equator
They are measured from 0 to 90 degrees north and south of the Equator
Latitude is also measured in degrees, minutes and seconds
Each minute of latitude represents 1 NM in distance

## Slide 28: Geographical Coordinates
The location of any object on the earth’s surface can be expressed by its relation to the lines of latitude and longitude
On most maps, the lines representing the meridians and parallels are numbered, and each tick on these lines represents one minute
The latitude of an object is always given first
i.e. N46° 21’ 10” W72° 40’ 46”
Notes: Montreal Map
Trois-Riviers Airport

## Slide 29
Longitude
Latitude

## Slide 30
50° 30’
Parallel of Latitude
N50° 26’
Meridian of Longitude
W104° 40’

## Slide 31: Time
The interval of time between the sun passing the same point is called a Solar Day
This solar day is divided into 24 hours
The problem with using this system to measure time is that the sun passes different points on the earth at different times

## Slide 32: Time and Longitude
24 hrs = 360° longitude
1 hr = 15° longitude
1 min = 15 min longitude
1 sec = 15 sec longitude
360° longitude = 24 hrs
1° longitude = 4 min
1 min longitude = 4 sec
1 sec longitude = 1/15 sec

## Slide 34: Coordinated Universal Time
To solve the solar day problem, the earth is divided into 24 time zones
These zones are referenced to the time zone with the prime meridian in it
The time in the reference time zone is known as Universal Coordinated time (UTC) or Zulu time
All time zones can be adjusted to match UTC
Winter time is the same as DAYLIGHT SAVINGS TIME

## Slide 35: Canadian Time Zones
Canada is divided into six time zones
They are:
Pacific = UTC +8(7)
Mountain = UTC +7(6)
Central = UTC +6(5)
Eastern = UTC +5(4)
Atlantic = UTC +4(3)
Newfoundland = UTC +3:30(2:30)
The numbers indicate how many hours must be added to the local time to get UTC during standard time. The numbers in brackets indicate the hours to be added during daylight savings time.

## Slide 36: Magnetic Variation
True north is the geographical top of the earth
Magnetic north is the direction the compass needle lies; is not a fixed point
Magnetic variation: the angle between a true meridian and the corresponding magnetic meridian (also known as declination)

## Slide 37: Magnetic Variation
The method of calculating magnetic heading from true heading is:
TRUE HEADING + WEST VARIATION = MAGNETIC HEADING
TRUE HEADING - EAST VARIATION = MAGNETIC HEADING
EAST IS LEAST
WEST IS BEST

## Slide 38: Compass Deviation
Compass deviation: angle between magnetic heading and the compass heading (magnetic heading corrected for deviation)
By using a compass correction card, we can determine the amount of error and add it to the magnetic heading
Notes: Swinging the compass:
Effect of deviation is corrected by “swinging the compass”. The aircraft is lined up on each bearing at 30 degree intervals and the compass heading is compared to the real direction. The differences are recorded on the compass correction card mounted in the cockpit as a reference

## Slide 39: Compass Deviation
The method of calculating compass heading from magnetic heading is:
MAGNETIC HEADING + WEST DEVIATION = COMPASS HEADING
MAGNETIC HEADING - EAST DEVIATION = COMPASS HEADING
EAST IS LEAST
WEST IS BEST

## Slide 40: Variation and Deviation
To remember which order to add or subtract headings, use the acronym
TVMDC
rue
ariation
agnetic
eviation
ompass
Two Violinists Make Dull Company

## Slide 41: Compass Errors
The magnetic compass is subject to many errors. These include:
Magnetic Dip
  The earth’s magnetic lines are parallel to the earth near the equator, but as one nears the magnetic poles, the lines become more vertical
  This causes the compass to dip towards the pole and can make it unreadable at high latitudes

## Slide 42: Compass Errors
Northerly Turning Error
  When an aircraft banks, so does the compass, and this can cause errors in the turn
  On turns from NORTH, the compass LAGS
  On turns from SOUTH, the compass LEADS

## Slide 43: Compass Errors
Acceleration Error
  When the aircraft accelerates, the compass dips slightly. This can cause it to indicate a turn on east and west headings
  Acceleration causes the compass to indicate a turn to the North
  Deceleration causes the compass to indicate a turn to the South

## Slide 44: Review
How many meridians of longitude are there?
What is a solar day?
What is acceleration error?
Notes: 24 meridians
Interval of the sun passing the same point
When an aircraft accelerates on an East or West heading, the compass will tend to indicate a turn towards the North

## Slide 45: The “One-in-Sixty’ Rule
This is a rule that can be used to help determine either how far you are off course or how much of a correction needs to be made to regain your course.
The rule states that
An error in the track of one degree will cause an error in position of about one mile in a distance of 60 miles
1°
1 mile
60 miles

## Slide 46: The ‘One-in-Sixty Rule’
The One-in-Sixty rule can be expressed as an equation
Where
e = Distance off Track
d = Distance Traveled
θ = Track Error

## Slide 47: The ‘One-in-Sixty Rule’
For example:
Track Error = 4°, Distance Traveled = 30 miles

## Slide 48: The ‘One-in-Sixty Rule’
The equation can also be arranged to find Track Error
Distance off track = 3 , Distance Traveled = 45 miles

## Slide 49: Track Correction Methods
Visual Alteration Method
  Compare ground to map
  Find landmark(s) along route
  Use landmark(s) to navigate back to intended track or towards destination

## Slide 50: Track Correction Methods
Double Track Error Method
  Use to return to intended track
  Used before the halfway point
Opening and Closing Angles Method
  Use to fly directly to the destination
  Can be used at any time a track error is noticed

## Slide 51: Tracks
Track
  The intended path of the aircraft over the ground
Track Made Good
  The actual path of the aircraft over the ground
Drift/Track Error
  The angle between the heading of the aircraft and the track made good

## Slide 52
Drift/Track Error

## Slide 53
Opening Angle
  The angle between the required track and the track made good
Closing Angle
  The angle between the old track and the new required track necessary to arrive at the destination

## Slide 54: Double Track Error Method
At (•) you are 4° right of your track after 10 mins
  Alter your track 4° left to parallel your track
  Alter your track 4° more left to intercept your track
After 10 mins using the 8° correction you intercept
Alter track 4° right to regain intended track

## Slide 55: Opening and Closing Angles Method
At (•) you are off track
  Your opening angle is 6° right of track
  Your closing angle is 8° to get to the destination
Add opening and closing angles (12°)
Subtract 12° to correct back to the left and go directly to destination

## Slide 56: Introduction to Maps

## Slide 57: Introduction to Maps
The surface of a sphere cannot be accurately projected onto a flat surface, so all maps show the surface of the earth with some degree of distortion
The two types of projections used for aviation maps are
  Lambert Conformal Conic Projection
  Mercator Projection

## Slide 58: Lambert Conformal Conic Projection
This projection is created by placing an imaginary cone over the earth, and then projecting the map onto the places where the cone touches the earth
Properties of the LCCP are
  Meridians of longitude converge towards the pole
  Parallels of latitude are concave towards the nearest pole
  Scale is virtually uniform
  A straight line is a GREAT CIRCLE
VNC, WAV and HI/LO enroute maps are based on this principle

## Slide 59: Mercator Projection
This projection is created by placing an imaginary cylinder over the earth so that the only place it’s touching is the equator
Properties of the Mercator Projection are
  Meridians of longitude are straight and parallel
  Parallels of latitude are straight and parallel
  There is no constant scale
  A straight line drawn on this map is a rhumb line
  Areas in high latitudes are greatly exaggerated
  Distances near equator are fairly precise
World map usually uses this principle

## Slide 60: Transverse Mercator Projection
This projection is created by placing the imaginary cylinder over the earth to touch the earth at only a chosen meridian
Used to cover a very small area
Properties similar to Mercator:
  Scale is precise regardless of latitude
  Longitude and latitude will appear curved if area coverage is wide enough
  Distance is precise along central meridian and throughout the map because the coverage area is so small
  Some distortion towards East and West margins of the map
VTA map is based on this principle

## Slide 61: Basic Elements of Maps
All maps are made up of four basic elements
AREAS
SHAPES
BEARINGS
DISTANCES

## Slide 62: Basic Properties of Maps
All aeronautical maps depict:
  Scale
  Relief
  Isogonic Lines
  Communities, roads and railways
  Aerodromes
  Restricted Areas
  Compass Rose
  Aeronautical Information
Notes: Symbols:
Isogonic lines: shown as dashed line with value printed at regular intervals
Settlements: Towns and villages are yellow squares or circles; cities and large towns are yellow with a black border corresponding to the real shape and size of the settlement
Highways: red or brown line and divided highways are double lines
Railways: black lines with hash marks through it
Aerodromes: small aerodromes are represented by a circle
Larger aerodromes with paved runways are represented in their precise location on the chart by a diagram of their runway layout
Restricted airspace: Circle or shape with hash marks on the inside of the outline
Include alert zones, danger areas, restricted airspace, advisory airspace, altitude reservations and military operation areas
Compass rose: circle divided into 360 degrees printed on chart centered on radio navigation aids (VOR and TACAN) can be used for measuring directions
Aeronautical data: legend explains all symbols and information found on the chart
Aerodrome data: next to the aerodrome symbol is a line leading to a box containing the name of the aerodrome. Under is information about elevation, lighting equipment, longest runway length, zone type and proper frequency
Obstructions: identified by a symbols; usually a tower with elevation in ASL and then (AGL)

## Slide 63: Scale
On aeronautical charts, scale is shown with two methods
Representative Fraction
  A fraction showing the size relationship between objects on the ground and objects on the map
  I.e. 1:500,000
Graduated Scale
  A scale printed on the side of the map that allows measurements on the map to be converted to actual distances (one in KM, one in SM and one in NM)
Notes: Scale: relationship between units of distance on the chart to the real distance on the Earth

## Slide 64: Relief
Relief is depicted in four ways on aeronautical charts:
Layer Tinting
  Different colours are used to represent areas of different elevation; water is always blue
Contour Lines
  Lines joining places of equal elevation on a chart
  The closer the contour lines, the steeper the slope
Notes: Known obstacles or groups of obstacles: elevations are indicated in ASL and AGL in parentheses

## Slide 65: Relief
Shading
  Shading is added to the sides of hills to give them the appearance of relief
Spot Heights
  Points of high elevation are depicted with a dot and the appropriate elevation
  The coordinates of the highest point on a chart are printed in the legend
Layer Tinting
Spot Heights
Shading
Contour Lines
MEF
Notes: Maximum Elevation Figure (MEF): a large number found at the centre of each section formed by lines of longitude and latitude.
Represents the highest terrain altitude within that section plus 328 feet/100 meters, or the highest obstacles known (whichever is higher) then rounded up to the next hundred of feet
Highest elevation on a chart:
The position and elevation of the highest point on the chart is found in the border over the layer tinting scale, which is found in the legend of the chart

## Slide 66: Review
What is the One-in-sixty rule?
What are the basic elements of maps?
What are the three types of projections?
Notes: A track error of 1 degree will result in an error of 1 mile off track in a distance 60 miles
Area Shapes Bearings Distances
Lambert Conic Conformal Projection Mercator Projection Transverse Mercator Projection

## Slide 67: Types of Aviation Charts

## Slide 68: VFR Navigation Chart (VNC)
Most commonly used chart for VFR navigation
Used mainly for slower speed aircraft flying at low altitudes
It has a scale of 1:500,000 and uses the Lambert Conformal Conic Projection
Notes: 1 inch = approximately 8 SM
Intended for visual navigation
Chart is printed on both sides
Each chart is designated by the name of its major feature (Toronto, Winnipeg, Montreal...)

## Slide 70: World Aeronautical Chart (WAC)
Mainly used for visual navigation at high speeds and high altitudes over long distances
Rarely used anymore
It has a scale of 1:1,000,000 and uses the Lambert Conformal Conic Projection
Notes: Intended for visual navigation

## Slide 72: VFR Terminal Area Chart (VTA)
Used for visual navigation in around airports which are surrounded by Class C airspace
They are printed for 6 airports in Canada (Toronto, Ottawa, etc.)
There scale is 1:250,000 and they use the Transverse Mercator Projection
Notes: VTA border are drawn on VNC maps to help the pilot identify where they are located and when he needs to refer to them
Contains calling in points and VFR standard procedure inside its boundary

## Slide 74: Low and High Enroute Charts
Low and high enroute charts (LO and HI) are used for IFR navigation
They depict very little ground detail, but depict a very detailed picture of the IFR airspace system
Scale is not constant between charts
Notes: Provide necessary information for radio navigation using the established airways
Designed for IFR use
Do not show cities, towns or geographic features (except major ones)
Show radio-navigation aids, IFR checkpoints, radio frequencies, etc.

## Slide 76: TC-AIM
Transport Canada Aeronautical Information Manual (TC-AIM)
Single source of information on rules of the air and other CARs
Subscription available for all pilots or free online at http://www.tc.gc.ca/CivilAviation/publications/tp14371/menu.htm
Notes: Developed to consolidate pre-flight reference information into a single primary document
Provides crews with single source for information concerning rules of the air and procedures for aircraft operation in CARs of interest to pilots
CARs-Canadian Aviation Regulations
TC-AIM has no legal value and juridical questions must be referred directly to CARs
Updates are published twice a year in April and October. Pilot’s responsibility to ensure document is up to date.
Subscriptions available, copies may be purchased from Transport Canada or available for free online.

## Slide 77: Canada Flight Supplement
Lists and provides information about all land aerodromes in Canada
Is updated every 56 days
Also provides information about preferred IFR routing, intercept orders, obstructions and other miscellaneous aeronautical data
Notes: Indicates diagram of aerodrome, layout of runways, placement of buildings and control tower, alphanumeric code of the aerodrome, geographic co-ordinates, magnetic variation, local time conversions, elevation of aerodrome, radio frequencies, services offered and various other information
Joint civil/military publication
Information on land and some water aerodromes and used as a reference for planning and safe conduct of air operations
Typically only provides information on aerodromes that:
-are open to the public
-used by more than one aircraft
-telephone available to aerodrome users
Information is only current to the date of submission for printing
NOTAMs amend or cancel the information in this document and must therefore be consulted to ensure that current information is sued for flight operation

## Slide 79: Flight Planning
Adequate and current aviation maps
Carefully prepared navigation
Flight plan or flight itinerary filed
Weather information
NOTAMs
Aircraft performance numbers
Calculate weight and balance
Perform complete passenger and crew briefing
Notes: Flight time: Time calculated from the moment the aircraft begins to move under its own power with the intention of taking off until the moment that the aircraft comes to a stop at the end of the flight.
Pre-flight inspection:
Pre-flight inspections must be performed in accordance with the manufacturer’s manual, checklists and school procedures before each flight. Verify the validity and conformity of documents carried on board with the requirements before flight and carry them on board.
Weight and Balance:
A weight and balance calculation using the graphs and tables in the POH must be carried out to ensure that the centre of gravity is within permissible limits and to determine if the aircraft is adequately loaded in accordance with the principles of FLIGHT SAFETY.

## Slide 80: Review
What is a great circle?
What are the types of charts used in aviation?
What can you find in the CFS?
Notes: Circle on the surface of the Earth whose plane passes through the centre of the Earth and cuts it into equal parts
VNC VTA WAC HI/LO enroute
Aerodrome name and identifier, elevation Runway orientation, length, composition Building and tower locations Frequencies Radio navigation facilities Lighting equipment Other aerodrome characteristics and facilities

## Slide 81: Summary
Topics covered today:
  Definitions
  Latitude and Longitude
  Earth’s Magnetism
  Compass Errors
  Projections
Next class will be airmanship and radios